## Slide 1: “Lords of the Sea” The Athenian Trireme A Design Challenge
Created by Laurie A. Bisconti,
redesigned for IEEE REACH

## Slide 2: The Purpose
To understand the tremendous difficulty to design a lightweight vessel such as the trireme that could carry a crew of 200 and maintain maximum speed and flexibility.

## Slide 3: The Problem
Design and build a floating structure to be tested in class to hold as much as possible before capsizing or sinking and travel with maximum speed through the water.

## Slide 4: Specifications
Vessel may consist of only foam core and glue/tape
  All materials provided in lab
Material used may not exceed 10” x 10”
Vessel must float
  Vessel may not rest on bottom of tank when tested
Vessel must have a “hook” (paper clip) on its bow

## Slide 5: Consider this
How will we know we have built the craft to hold the maximum cargo load?

## Slide 6: Planning
Use the following slides to complete your sketches and calculations in your packet

## Slide 7: What is displacement???
Pools
Bathtubs
Kitchen Sinks
Turkey Fryers

## Slide 8: Sketch your vessel

## Slide 9: Dimension your vessel Length – Width – Height
2”
4”
3”

## Slide 10: Determine Volume of Barge
2”
4”
3”
Length x Width x Height = 24 cu in

## Slide 11: How many inches in a cubic foot?
1728

## Slide 12: Divide Barge Volume by the # of cubic inches in a cubic foot.
24cu” / 1728 = .013 cubic feet
2”
4”
3”

## Slide 13: The weight of water
64 pounds per cubic foot

## Slide 14: Determine pounds of water displaced by the barge.
Multiply Cu. Ft. of barge by weight of water per cubic foot
.013 x 64 = .832 pounds displaced

## Slide 15: Determine the mass of the barge
2”
4”
3”
Approximately 100 grams

## Slide 16: How many grams are in a pound?
1 pound = 453.6 grams

## Slide 17: Convert grams to pounds
100 / 453.6 = .22 pounds

## Slide 18: Subtract weight of barge from weight of displaced water to find penny load.
.832 - .22 = .612 pounds of pennies

## Slide 19: Convert penny load lbs into mass
.612 x 453.6 = 277 grams of pennies

## Slide 20: What is the mass of a penny?
2.78 grams

## Slide 21: Divide allowable penny mass by the mass of one penny to determine the number of pennies the barge can hold
277 / 2.78 = 99 pennies

## Slide 22: Why could this number be less?
Workmanship
Loading
Other variables

## Slide 23: Now that you have a plan
You and your design team will meet to build your vessel.